## Slide 1: Homecoming float construction safety orientation
Baylor University
2019
Ken O’Connor
Department of Environmental Health & Safety

## Slide 2: General Recommendations
The float chairman must be responsible for the safety of the students working on the float
Use the buddy system…never work alone
In case of emergency call 9-1-1 (off campus)
  If on campus, call 710-2222 (BU PD) for fastest response
If there is an accident resulting in injury, please let me know via Baylor’s online incident reporting system.
  www.baylor.edu/ehs/

## Slide 3: General Recommendations
NEVER assume people know how something works
Wear Proper Attire
  No open shoes
  No shorts
  No synthetic fabrics
  Long hair contained (ties back, hat, etc.)
Recommended Personal Protective Equipment (PPE)
  Safety glasses, closed ended shoes, leather gloves
Have a First-Aid Kit on hand
  Bandages, gauze, antiseptic ointments or sprays
    If possible, always have injured person treat own injury
    Sterile disposable gloves
  Something to treat insect bites (ointments, sprays, Benadryl)
  First aid burn cream
  Don’t let just anyone use powered equipment or welding/cutting equipment

## Slide 4: General Safety
Keep your construction area clean and organized.
Take ventilation of your site seriously, especially if using a gas powered generator, painting, or using solvents and paint thinners

## Slide 5: THE most important thing to address on day one of construction
How to Access to trailer bed
How do we build a float on this
Prevent this 

## Slide 7: Electrical Safety
Reality Check:
  Annually in US: 30,000 non-fatal shocks  4400 required visit to emergency rooms  400 required visit to morgue
  The #1 cause of structure fires in the US.
Do not mix water and electricity
Don’t overload the outlets
  Typical receptacle is 15 A. A typical circular caw pulls 13.
Don’t use damaged or poor quality equipment, especially extension cords.

## Slide 8: Angle Grinder
HAZARDS
  Metal lodging in the eye (MOST COMMON)
  Kickback can result in severe cuts to body and legs
  Discs can shatter, sending pieces flying across workshop
  Sparks can act as an ignition source
SAFE GUARDS
  Wear goggles, or safety glasses+face shield
  Use the correct type of disc (cutting versus grinding; different discs for different materials)
  Make sure guards are in place and disc is undamaged
  Remove flammables from work area

## Slide 9: Circular Saw, Chop Saw, Miter Saws
HAZARDS
  Eye injuries
  Amputation
Safe Guards
  Ensure guards are in place
  Wear eye protection
  Keep hands out of cutting zone. Even with guard in place, part of saw blade could be exposed.
  Follow all recommendations in the OEM’s operating manual
Blade Guard

## Slide 10: Welding and Cutting
Area assessment
  Remove all combustible materials and flammable liquids within 35’.
    Oily rags, saw dust, paper & cardboard
    Flammable liquids should be kept in a fire cabinet, or as far back from ignition sources as possible.
Fire Protection
  Need a minimum one 5 lb. ABC fire extinguisher
  Fire watch (during welding and before leaving for the day)

## Slide 11: Welding - PPE
Welding helmet
Safety glasses
Welding jacket
Welding cap
Welding gloves
Heavy denim pants
Leather boots
Welding Curtain

## Slide 12: Float Inspection Schedule and Additional Recommendations
Inspection Schedule
  One month out
  One week out
  Day prior
DC Batteries are preferred over gas powered generators
    If using a generator, exhaust must be vented away from the float
    Can not have any combustibles (pomping in particular) with in 12” of the vent pipe/hose
Fireproofing of pomping and other highly combustible materials is a requirement
    UL Classified Class “A” Fire Retardant
    Follow the directions for appropriate coverage and perform a few tests yourself
Questions??? Contact info:
KENNETH_OCONNOR@BAYLOR.EDU
254-709-7383 (C)